## Slide 1: Hauptseminar Rechnerarchitektur und Programmierung
Zentrum für Informationsdienste und Hochleistungsrechnen (ZIH)
Adapteva Parallella:
Crowd-funded Low-budget Open-source HPC

## Slide 2: Structure
  The Adapteva Parallella Platform
    Company history of Adapteva
    Motivation
    The Parallella board
    The Epiphany coprocessor
  Implementation of the 1D-FFT with filtering
    Motivation
    Implementation details
    Performance results
  Comparison with current architectures - GPUs
  Assessing the Parallella's potential for HPC
2

## Slide 3: Company History of Adapteva
  Feb 2008: Founded by Andreas Oloffson
    Goal: 10 times advancement in floating point processing energy efficiency
  Jun 2009: Tapeout of Epiphany-I prototype (65nm)
    Secured 1.5M US$ in Series-A funding from Bittware
  May 2011: Sampled Epiphany-III (65nm) product
  Aug 2012: Demonstration of 50 GFLOPS/Watt efficiency at 28nm
  Oct 2012: Launch of Parallella kickstarter project
  Jul 2013: first Parallella boards shipped to Kickstarter backers
  Apr 2014: Completed shipping of all Parallella boards to Kickstarter backers
3

## Slide 4: Parallella Kickstarter Program
  Slogan: “The parallella project will make parallel computing accessible to everyone”
  Kickstarter project gained 898,921$ from 4,965 backers
  Attributes:
    Open Access: no NDAs or special access needed
    Open Source: platform based on free open source development tools and libraries
    Affordable: Parallella high performance computer at costs below 100$
 Close the knowledge gap in parallel programing
 Democratize access to parallel computing
4

## Slide 5: Motivation for Epiphany Multicore Architecture
5

## Slide 6: Parallella Board
6
  Tech specs:
  Dual-core ARM A9
  16-core Epiphany Coprocessor
  1 GB RAM
  MicroSD Card
  USB 2.0
  Gigabit Ethernet
  Linux
  Peak Performance: 26 GFLOP/s (single precision)
  2 Watt Energy Consumption

## Slide 7: System Overview of Parallella Board
7

## Slide 8: High Level Overview of the Epiphany Architecture
8

## Slide 9: eMesh Network on Chip
9
  Attributes:
  Only nearest neighbor connections
  Connections to North, East, South and West
  1.5 clock cycles latency per hop (write)
  Three separate orthogonal networks:
    cMesh: used for on-chip write transactions
    xMesh: used for off-chip write transactions
    rMesh: used for all read requests

## Slide 10: Memory Scheme of the Epiphany Architecture
10
  Attributes:
  Flat 32 bit address space split into 4096 1-MiB chunks
  Each core is assigned his own 1-MiB chunk
    But has transparent access to memory of any other core
  Optimal performance only if data is placed in local memory banks
  Magic address translation – each core can access all memory locations

## Slide 11: Example: Parallella as a Cluster
  Boards can be combined to one cluster
  Gigabit-Ethernet interconnect
   With thousands of boards put together you can build a supercomputer at low cost
11

## Slide 12: Future Ideas for Epiphany Architecture
12

## Slide 13: Motivation: Implementation of the 1D-FFT on Epiphany
  Fast Fourier Transform is basic operation for many applications
  Algorithm to compute the discrete fourier transform
  Concrete example: Filtered backprojection as CT-Reconstruction algorithm
FFT + Filtering
+ Inverse FFT
Backprojection
Implementation on Parallella
13

## Slide 14: Implementation details
14
  Attributes:
  Sinogram is divided into lines
    16 cores calculate 64 lines in parallel to transfer as much data as possible
Read Tif-Image
…
Data Transfer
(serial)
…
Computation
Data Transfer
(serial)
Write Tif-Image
16x
Repeat until all lines are done
Hostprocessor
Epiphany-Coprocessor
16x
…
16x

## Slide 15: Data Transfer vs Calculation Time (1 core)
  Data transfer is the main bottleneck
  To increase performance, more calculation per memory transfer is necessary
  Due to Amdahls law speedup cannot exceed 2.5 with 16 cores
  Maximum speedup of 2.9 possible
  TODO: reason
15
Chart: 
| write | read | calculation
 | 0.07002 | 0.14551 | 0.39353

## Slide 16: Performance Results
  Results measured for 500 FFTs of size 256
  Small memory transfer rate to local memory banks
  Read = read + write  half performance compared to write
16
 | 1 core | 16 cores
Write Time | 70 ms | 72 ms
Computation Time | 394 ms | 25 ms
Read Time | 146 ms | 148 ms
Number of Foating Point Operations |  | 
MFLOP/s in Computation Part | 35 MFLOP/s | 556 MFLOP/s
MFLOP/s in whole Program | 23 MFLOP/s | 57 MFLOP/s
Transfer Rate: Write | 14,6 MByte/s | 14,2 MByte/s
Transfer Rate: Read | 7,01 MByte/s | 6,9 MByte/s
 | 1 core | 16 cores
Write Time | 70 ms | 72 ms
Computation Time | 394 ms | 25 ms
Read Time | 146 ms | 148 ms
Number of Foating Point Operations |  | 
MFLOP/s in Computation Part | 35 MFLOP/s | 556 MFLOP/s
MFLOP/s in whole Program | 23 MFLOP/s | 57 MFLOP/s
Transfer Rate: Write | 14,6 MByte/s | 14,2 MByte/s
Transfer Rate: Read | 7,01 MByte/s | 6,9 MByte/s

## Slide 17: Speedup of parallelisable Calculation Part
Chart: Number of cores
| 1 | 2 | 3 | 4 | 6 | 8 | 9 | 12 | 16
Speedup | 1 | 2.0021 | 2.9662 | 3.965 | 5.9671 | 7.819 | 8.9459 | 11.9614 | 15.6598
Maximum possible speedup | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
17

## Slide 18: Overall Speedup
Chart: Number of cores
| 1 | 2 | 3 | 4 | 6 | 8 | 9 | 12 | 16
Speedup | 1 | 1.4834 | 1.75 | 1.9423 | 2.1614 | 2.2574 | 2.3415 | 2.4478 | 2.4874
Maximum possible speedup according to Amdahl's Law | 1 | 1.4772 | 1.7567 | 1.9402 | 2.07 | 2.1666 | 2.2413 | 2.3008 | 2.3493 | 2.3896 | 2.4236 | 2.4527 | 2.4779 | 2.4998 | 2.5192 | 2.5364
18

## Slide 19: Excursion: Memory Bandwidth
19
Chart: Data[Bytes]
| 1 | 8 | 16 | 32 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 6144 | 8192
Bandwidth Write | 12.54 | 26.92 | 28.6 | 29.15 | 29.6 | 29.7 | 29.75 | 29.75 | 29.76 | 29.78 | 29.75 | 29.76
Bandwidth Read | 6.27 | 13.15 | 13.32 | 13.4 | 13.5 | 13.5 | 13.5 | 13.5 | 13.55 | 13.57 | 13.5 | 13.5

## Slide 20: Comparison with current Architecture - GPUs
  Comparison with Intel Core i7 2600 combined with Nvidia Geforce 750Ti in terms of energy efficiency
  Identical implementation with use of cufft-Library from Nvidia
Peak Performance Single Precision | 1,472 TFLOP/s
Number of Streaming Multiprocessors (SMs) | 5
Number of cuda cores | 640
Memory Bandwidth | 86,4 GByte/s
Architecture | Maxwell
Memory bus interface | 128 Bit
Manufacturing Process | TSMC 28nm
Thermal Design Power (TDP) | 60 Watt
Launch Date | 02/18/14
Die size | 148
Peak Performance Single Precision | 1,472 TFLOP/s
Number of Streaming Multiprocessors (SMs) | 5
Number of cuda cores | 640
Memory Bandwidth | 86,4 GByte/s
Architecture | Maxwell
Memory bus interface | 128 Bit
Manufacturing Process | TSMC 28nm
Thermal Design Power (TDP) | 60 Watt
Launch Date | 02/18/14
Die size | 
20

## Slide 21: Comparison of Parallella with GeForce 750 Ti
  To stay fair comparison in terms of energy efficieny and chip area
  Energy consumption/Picture [mWs]:
  Initialization phase of cuFFT very time consuming
  Due to low memory size, and small memory bandwidth, GPU can outperform Parallella in terms of energy efficiency in this case
21
Number of Pictures | Parallella | GPU
1 | 510 | 10200
100 | 510 | 114
1000 | 510 | 18,6

## Slide 22: Comparison in Terms of Chip Area
  Example configuration of Epiphany with 1024 cores:
  Comparable to NVIDA Geforce 750 TI in terms of die size
22
Number of cores | 1024
Manufacturing Process | 28 nm
Max. Operating Frequency | 700 MHz
Peak Performance (Single Precision) | 1,408 GFLOP/s
Die size | 131
Thermal Design Power | 20 Watt
Number of cores | 1024
Manufacturing Process | 28 nm
Max. Operating Frequency | 700 MHz
Peak Performance (Single Precision) | 1,408 GFLOP/s
Die size | 
Thermal Design Power | 20 Watt

## Slide 23: Assessing the Parallella's Potential for HPC
  Pros:
    Interesting architecture
  Cons:
    Memory transfer bottleneck
    Small local memory size
23

## Slide 24: Thank you